## Slide 1
Horse Heartbeats: ECG, HRV, and a Van der Pol Model of Rhythm
What you’ll learn:
Identify R-peaks in a Polar Equine ECG and recognize motion artifact.
Compute HR from RR/NN intervals and quantify HRV with SDNN and RMSSD.
See how noise and missed/extra beats can distort HRV—and how to choose clean segments.
Use a Van der Pol oscillator to model rhythmic beats and explore how parameters create variability.
Notes: [Sources] - HRV definition & common time-domain metrics: Task Force standards (Circulation, 1996). https://pubmed.ncbi.nlm.nih.gov/8598068/ [/Sources]

## Slide 2
The mammalian heart
The mammalian heart is a four-chambered pump with four main valves: the tricuspid, pulmonary, mitral, and aortic valves.
The chambers are the right and left atria and the right and left ventricles.
The atria receive blood returning to the heart and help fill the ventricles.
The right ventricle pumps blood to the lungs.
The left ventricle pumps blood to the body.
Each heartbeat is initiated by the heart’s electrical pacemaker—usually the sinoatrial (SA) node.
EquiPhysics – equiphysics.org
Horse Heartbeats Lab
Notes: [Sources] - Definition of HRV and interpretation framework (time-domain, frequency-domain): Task Force standards (Circulation, 1996). https://pubmed.ncbi.nlm.nih.gov/8598068/ - Factors influencing equine HRV during rest/exercise/recovery: Younes et al., Frontiers in Physiology (2016). https://www.frontiersin.org/articles/10.3389/fphys.2016.00155/full [/Sources]

## Slide 3
Electrocardiogram (ECG)
Electrocardiography (ECG) is a diagnostic tool used to measure the electrical activity of the heart. An ECG machine records the electrical signals from the heart and produces an ECG waveform, which is a graphical representation of the heart’s electrical activity.
https://medtigo.com/blog/how-do-you-interpret-ecg-values/
EquiPhysics – equiphysics.org
Horse Heartbeats Lab
Notes: [Sources] - Definition of HRV and interpretation framework (time-domain, frequency-domain): Task Force standards (Circulation, 1996). https://pubmed.ncbi.nlm.nih.gov/8598068/ - Factors influencing equine HRV during rest/exercise/recovery: Younes et al., Frontiers in Physiology (2016). https://www.frontiersin.org/articles/10.3389/fphys.2016.00155/full [/Sources]

## Slide 4
Electrocardiogram (ECG)
https://medtigo.com/blog/how-do-you-interpret-ecg-values/
P wave – The P wave represents the electrical activity that occurs when the atria contract to pump blood into the ventricle.
QRS complex – The QRS complex represents the electrical activity that occurs when the ventricles contract to pump blood out of the heart.
T wave – The T wave represents the electrical activity that occurs when the ventricles are repolarizing (returning to their resting state) after contraction.
U wave – The U wave is a small waveform that sometimes appears after the T wave. Its significance is not well understood.
EquiPhysics – equiphysics.org
Horse Heartbeats Lab
Notes: [Sources] - Definition of HRV and interpretation framework (time-domain, frequency-domain): Task Force standards (Circulation, 1996). https://pubmed.ncbi.nlm.nih.gov/8598068/ - Factors influencing equine HRV during rest/exercise/recovery: Younes et al., Frontiers in Physiology (2016). https://www.frontiersin.org/articles/10.3389/fphys.2016.00155/full [/Sources]

## Slide 5
Electrocardiogram (ECG)
EquiPhysics
EquiPhysics • Weekly Duque Routine
https://medtigo.com/blog/how-do-you-interpret-ecg-values/
Heart rate – The heart rate can be determined by calculating the number of QRS complexes per minute. A normal human heart rate is between 60 and 100 beats per minute.
Rhythm – The rhythm of the heartbeat can be determined by analyzing the spacing between each QRS complex.
NN interval – The time gaps between consecutive normal heartbeats.
RR interval – The time gaps between consecutive R waves.
Notes: [Sources] - Definition of HRV and interpretation framework (time-domain, frequency-domain): Task Force standards (Circulation, 1996). https://pubmed.ncbi.nlm.nih.gov/8598068/ - Factors influencing equine HRV during rest/exercise/recovery: Younes et al., Frontiers in Physiology (2016). https://www.frontiersin.org/articles/10.3389/fphys.2016.00155/full [/Sources]

## Slide 6
Electrocardiogram (ECG)
EquiPhysics
EquiPhysics • Weekly Duque Routine
Characteristic aspect of base-apex ECG in horses (Colin, 2005)
Notes: [Sources] - Definition of HRV and interpretation framework (time-domain, frequency-domain): Task Force standards (Circulation, 1996). https://pubmed.ncbi.nlm.nih.gov/8598068/ - Factors influencing equine HRV during rest/exercise/recovery: Younes et al., Frontiers in Physiology (2016). https://www.frontiersin.org/articles/10.3389/fphys.2016.00155/full [/Sources]

## Slide 7
What is normal for a horse?
EquiPhysics – equiphysics.org
Horse Heartbeats Lab
Pella Vet
Notes: [Sources] - Definition of HRV and interpretation framework (time-domain, frequency-domain): Task Force standards (Circulation, 1996). https://pubmed.ncbi.nlm.nih.gov/8598068/ - Factors influencing equine HRV during rest/exercise/recovery: Younes et al., Frontiers in Physiology (2016). https://www.frontiersin.org/articles/10.3389/fphys.2016.00155/full [/Sources]

## Slide 8
What is extreme?
EquiPhysics – equiphysics.org
Horse Heartbeats Lab
Notes: [Sources] - Definition of HRV and interpretation framework (time-domain, frequency-domain): Task Force standards (Circulation, 1996). https://pubmed.ncbi.nlm.nih.gov/8598068/ - Factors influencing equine HRV during rest/exercise/recovery: Younes et al., Frontiers in Physiology (2016). https://www.frontiersin.org/articles/10.3389/fphys.2016.00155/full [/Sources]

## Slide 9
What is extreme?
EquiPhysics – equiphysics.org
Horse Heartbeats Lab
https://training.arioneo.com/en/heart-rate/
Notes: [Sources] - Definition of HRV and interpretation framework (time-domain, frequency-domain): Task Force standards (Circulation, 1996). https://pubmed.ncbi.nlm.nih.gov/8598068/ - Factors influencing equine HRV during rest/exercise/recovery: Younes et al., Frontiers in Physiology (2016). https://www.frontiersin.org/articles/10.3389/fphys.2016.00155/full [/Sources]

## Slide 10
Van der Pol (VdP) Model
EquiPhysics • Weekly Duque Routine
Slide 2
The Van der Pol (VdP) model describes a nonlinear oscillator originally proposed to model self-sustaining electrical circuits.
In biological systems, it is often used as a simplified model of the heartbeat or other rhythmic physiological processes.
The VdP oscillator is a minimal mathematical way to capture the most essential feature of the heartbeat: a self-sustained, repeating rhythm.
The core idea: a stable “limit cycle” = a repeating heartbeat.
X(t) represents the membrane voltage
  can also be taken as a proxy for ventricular pressure
Y(t) represents its rate of change.
m is a parameter that controls the relaxation of the oscillation.
,
EquiPhysics – equiphysics.org
Notes: [Sources] - Definition of HRV and interpretation framework (time-domain, frequency-domain): Task Force standards (Circulation, 1996). https://pubmed.ncbi.nlm.nih.gov/8598068/ - Factors influencing equine HRV during rest/exercise/recovery: Younes et al., Frontiers in Physiology (2016). https://www.frontiersin.org/articles/10.3389/fphys.2016.00155/full [/Sources]

## Slide 11
Van der Pol (VdP) Model
EquiPhysics
For 𝜇 > 0, the system has a stable limit cycle: trajectories converge to the same closed loop regardless of initial conditions.
Physiologically, it’s analogous to the heart’s robust periodic rhythm.
When is moderately large, the waveform becomes a relaxation oscillation:
  Slow phase + fast jump + slow phase + fast jump
That maps naturally onto heart-cycle asymmetry:
  Diastole (filling) is typically the longer, slower part of the cycle.
  Systole (ejection/contraction) is shorter and faster.
https://latexdraw.com/phase-portrait-of-van-der-pol-oscillator/
Horse Heartbeats Lab
Notes: [Sources] - Definition of HRV and interpretation framework (time-domain, frequency-domain): Task Force standards (Circulation, 1996). https://pubmed.ncbi.nlm.nih.gov/8598068/ - Factors influencing equine HRV during rest/exercise/recovery: Younes et al., Frontiers in Physiology (2016). https://www.frontiersin.org/articles/10.3389/fphys.2016.00155/full [/Sources]

## Slide 12
What is Heart Rate Variability (HRV)?
What Does HRV Tell Us?
Higher HRV is associated with lower stress levels in humans and other animals.
Heartbeat coupling and synchronized HRV between humans and horses.
HRV synchronization flows both ways—from human to horse and from horse to human.
EquiPhysics – equiphysics.org
Horse Heartbeats Lab
https://www.tres.in/health-insight/heart-rate-variability-does-it-matter/
Notes: [Sources] - Definition of HRV and interpretation framework (time-domain, frequency-domain): Task Force standards (Circulation, 1996). https://pubmed.ncbi.nlm.nih.gov/8598068/ - Factors influencing equine HRV during rest/exercise/recovery: Younes et al., Frontiers in Physiology (2016). https://www.frontiersin.org/articles/10.3389/fphys.2016.00155/full [/Sources]

## Slide 13
What is Heart Rate Variability (HRV)?
What is HRV?
The measure of variation in time between consecutive heartbeats (the Inter-Beat Interval, or IBI). It is not the same as heart rate.
What Does it Tell Us?
HRV reflects the balance between the sympathetic (stress, "fight-or-flight") and parasympathetic (calm, "rest-and-digest") branches of the autonomic nervous system.
It is a key, non-invasive metric for assessing physiological stress and animal welfare.
A reduction in HRV is often associated with a stress response.
EquiPhysics – equiphysics.org
Horse Heartbeats Lab
Notes: [Sources] - Definition of HRV and interpretation framework (time-domain, frequency-domain): Task Force standards (Circulation, 1996). https://pubmed.ncbi.nlm.nih.gov/8598068/ - Factors influencing equine HRV during rest/exercise/recovery: Younes et al., Frontiers in Physiology (2016). https://www.frontiersin.org/articles/10.3389/fphys.2016.00155/full [/Sources]

## Slide 14
Why measure HR + HRV?
HR tells us fast or hard the heart is working. HRV helps interpret how the body is responding.
Heart Rate (HR)
Increases with workload: speed + effort + terrain
Fitness shows up as lower HR for same work
Recovery HR: how quickly a horse returns toward baseline
Heart Rate Variability (HRV)
Beat‑to‑beat timing variation (R‑R intervals)
Higher HRV is associated with lower stress levels
Most useful when measured in rest and recovery
EquiPhysics – equiphysics.org
Horse Heartbeats Lab
Notes: [Sources] - Definition of HRV and interpretation framework (time-domain, frequency-domain): Task Force standards (Circulation, 1996). https://pubmed.ncbi.nlm.nih.gov/8598068/ - Factors influencing equine HRV during rest/exercise/recovery: Younes et al., Frontiers in Physiology (2016). https://www.frontiersin.org/articles/10.3389/fphys.2016.00155/full [/Sources]

## Slide 15
HRV metrics (and what they mean)
Metric
Layman description
Best use
RMSSD
Root Mean Square of Successive Differences: How much one beat interval changes compared with the next.
It’s relatively robust for short recordings and is commonly used in daily readiness/recovery tracking.
SDNN
Standard Deviation of NN intervals: Overall variability across the whole segment you’re analyzing
Longer resting windows; not ideal in noisy exercise data.
Mean HR
Average heart rate for a segment.
Workload + recovery speed.
Important: HRV metrics are sensitive to artifacts (missed/extra beats) — clean data matters.
NN intervals
The time gaps between consecutive normal heartbeats.
Best to use because the beats are coming from the heart’s normal rhythm, not a premature beat or an artifact.
Horse Heartbeats Lab
EquiPhysics – equiphysics.org
Notes: [Sources] - HRV metric definitions (RMSSD, SDNN) and interpretation: Task Force standards (Circulation, 1996). https://pubmed.ncbi.nlm.nih.gov/8598068/ - Equine HRV collection/analysis considerations (including artifacts/arrhythmias): Mitchell et al. (2021) review. https://www.sciencedirect.com/science/article/pii/S1090023320301672 [/Sources]

## Slide 16
From ECG to heart rate: R-peaks and RR intervals
Horse Heartbeats Lab
ECG signal
voltage vs time
R-peak times
t₀, t₁, t₂, …
RR intervals
RRₙ = tₙ − tₙ₋₁
If RR intervals vary from beat to beat, the *instantaneous* heart rate varies too.
That variation is the raw material for HRV.
EquiPhysics – equiphysics.org
Notes: [Sources] - https://archive.physionet.org/tutorials/hrv/ (RR intervals → HR/HRV tutorial) [/Sources]

## Slide 17
Calculating SDNN and RMSSD (time-domain HRV)
Horse Heartbeats Lab
Inputs
Use NN (normal-to-normal) intervals: RR₁, RR₂, …, RRₙ (after removing artifacts/ectopic beats).
Units are often ms.
Formulas
Step-by-step
1) Compute the mean RR ()
2) SDNN: take the sample standard deviation of RR
3) Compute successive differences: ΔRRₙ = RRₙ − RRₙ₋₁
4) RMSSD: square ΔRR, average, then take the square root
Worked example
Example NN intervals (ms):
n: 1 2 3 4 5
RR: 1000 980 1020 990 1010
ΔRR: -20 40 -30 20
Mean RR = 1000 ms
SDNN:
deviations: 0, −20, 20, −10, 10
squares sum = 1000
SDNN = √(1000/4) = 15.8 ms
RMSSD:
squares of ΔRR: 400, 1600, 900, 400
sum = 3300
RMSSD = √(3300/4) = 28.7 ms
EquiPhysics – equiphysics.org
Notes: [Sources] - https://www.ahajournals.org/doi/10.1161/01.cir.93.5.1043 (1996 Task Force; definitions of SDNN and RMSSD) - https://archive.physionet.org/tutorials/hrv-toolkit/ (time-domain HRV measures; practical computation notes) [/Sources]

## Slide 18
Modified Van der Pol (VdP) Model
The VdP model is deterministic, and HRV = 0.
To model HRV, we will modify the constant restoring term, −𝑋, with a time-varying restoring strength, −𝜔(𝑡)𝑋.
  This makes the system non-autonomous, so the oscillator’s cycle timing can change over time.
We define the time-dependent parameter as a sinusoidal modulation: ω(t) = ω0​+a sin(2πfm​t).
When a = 0, the oscillator beats at a steady rate.
When a > 0, the instantaneous frequency oscillates, which fluctuates the heart rate.
w0 controls the baseline heart rate
a is the amplitude of frequency modulation (which controls HRV strength)
fm is the modulation frequency, which sets the timescale of variability.
Horse Heartbeats Lab
EquiPhysics – equiphysics.org
Notes: [Sources] - Definition of HRV and interpretation framework (time-domain, frequency-domain): Task Force standards (Circulation, 1996). https://pubmed.ncbi.nlm.nih.gov/8598068/ - Factors influencing equine HRV during rest/exercise/recovery: Younes et al., Frontiers in Physiology (2016). https://www.frontiersin.org/articles/10.3389/fphys.2016.00155/full [/Sources]

## Slide 19
How do we measure HR and HRV?
EquiPhysics – equiphysics.org
The Polar V800 heart rate monitor is a system validated for collecting accurate Inter-Beat Interval (IBI) data in horses.
How it Works:
An electrode belt is placed around the horse's girth, near the elbow, to capture the heart's electrical signals.
It records beat-to-beat (R-R interval) data, which is essential for both heart rate and HRV analysis.
Horse Heartbeats Lab
Notes: [Sources] - Definition of HRV and interpretation framework (time-domain, frequency-domain): Task Force standards (Circulation, 1996). https://pubmed.ncbi.nlm.nih.gov/8598068/ - Factors influencing equine HRV during rest/exercise/recovery: Younes et al., Frontiers in Physiology (2016). https://www.frontiersin.org/articles/10.3389/fphys.2016.00155/full [/Sources]

## Slide 20
Interpreting the ECG and noise
Horse Heartbeats Lab
EquiPhysics – equiphysics.org
The Polar Equine strap gives an ECG-like waveform where each heartbeat shows up as a sharp R-peak (the big spike).
HR and HRV come from the timing between R-peaks (RR/NN intervals), not from the exact shape of the wave.
You may see small baseline wiggles and a fuzzy trace, but the R-peaks stay clear and consistently shaped.
Notes: [Sources] - Definition of HRV and interpretation framework (time-domain, frequency-domain): Task Force standards (Circulation, 1996). https://pubmed.ncbi.nlm.nih.gov/8598068/ - Factors influencing equine HRV during rest/exercise/recovery: Younes et al., Frontiers in Physiology (2016). https://www.frontiersin.org/articles/10.3389/fphys.2016.00155/full [/Sources]

## Slide 21
Interpreting the ECG and noise
Horse Heartbeats Lab
EquiPhysics – equiphysics.org
band is moving
The waveform can jump, saturate, or wander dramatically; sometimes the true ECG is partially buried.
This is dominated by electrode contact changes (strap slip, pressure changes, sweat conductivity shifts) →
  This causes large amplitude spikes and baseline shifts that are not heartbeats.
Peak detection can fail: you may get false R-peaks (too many beats) or missed beats (too few).
  This can create RR intervals that are unrealistically short/long.
Notes: [Sources] - Definition of HRV and interpretation framework (time-domain, frequency-domain): Task Force standards (Circulation, 1996). https://pubmed.ncbi.nlm.nih.gov/8598068/ - Factors influencing equine HRV during rest/exercise/recovery: Younes et al., Frontiers in Physiology (2016). https://www.frontiersin.org/articles/10.3389/fphys.2016.00155/full [/Sources]

## Slide 22
Connecting model ↔ data
Horse Heartbeats Lab
Van der Pol (model)
• Deterministic equations → a clean limit cycle
• μ tunes waveform shape (sinusoid ↔ relaxation)
• Phase plane tools: nullclines, vector field
• Great for intuition about self-sustained rhythms
ECG (data)
• Measurements include noise + artifacts
• Rhythm can change with gait, arousal, respiration
• HRV metrics summarize variability (not a full model)
• Preprocessing decisions matter (filters, peak detection)
⇄
Compare
patterns
Notes: [Sources] - https://www.scholarpedia.org/article/Van_der_Pol_oscillator (limit cycle behavior) - https://archive.physionet.org/tutorials/hrv/ (RR/HRV overview; preprocessing context) - https://commons.wikimedia.org/wiki/File:VanDerPolOscillator.png (image) - https://commons.wikimedia.org/wiki/File:SinusRhythmLabels.svg (image) [/Sources]

## Slide 23
Questions?
Github link for Python notebook:
https://github.com/equiphysics/education/tree/main/labs/horse_heart_VdP
Google Drive link for data: https://drive.google.com/drive/folders/1C8C6YqzpEVCts-inkqRmkxJYjD3-ahws?usp=drive_link
Video presentation: https://drive.google.com/file/d/1tHT9_Ju7jsudICALo1g34ZxiFcQ3Ok6a/view?usp=drive_link
How to use Python Notebook: https://drive.google.com/file/d/17JnD0S1rnOVXyJGxOd_vPU73z00aQq4S/view?usp=drive_link
Disclaimer: This content is educational and not a veterinary diagnosis.
Horse Heartbeats Lab
EquiPhysics – equiphysics.org
Notes: [Sources] - HRV standards and definitions: Task Force (Circulation, 1996). https://pubmed.ncbi.nlm.nih.gov/8598068/ - Equine HRV measurement considerations (artifacts, arrhythmias): Mitchell et al. (2021) review. https://www.sciencedirect.com/science/article/pii/S1090023320301672 [/Sources]